## Slide 1: 011144 Computer Networks
Exercise 3

## Slide 2
1. Which one is NOT provided by TCP/UDP (multiple choices)
  (a) flow control
  (b) connection setup and teardown
  (c) delay guarantee
  (d) congestion control
  (e) loss recovery
  (f) bandwidth reservation
  (g) in-order delivery
Ans: ()()

## Slide 3
2. Compute 8-bit checksum for 01100010 and 10111001, and use an example to show that if the two numbers each has a 1-bit error, the checksum can not detect the error.

## Slide 4
3. Host A sets up a TCP connection with Host B, fill in the blanks the appropriate acknowledgement numbers.

## Slide 6
4. Consider the following cwnd evolution at a TCP sender:

## Slide 7
  Is this TCP Tahoe or TCP Reno?
  What is the sender’s initial ssthresh?
  What happens at time 10? What is ssthresh and cwnd at time 11?

## Slide 8
  What happens at time 22? What is ssthresh and cwnd at time 23?
  Ans: Triple duplicate ACK, ssthresh = 12 MSS, cwd = 15 MSS
  What happens at time 36? What is ssthresh and cwnd at time 37?
  Ans: Timeout, ssthresh = 14 MSS, cwnd = 1 MSS.
  When is the 50th segment is sent?
  Ans: Time 6.

## Slide 9
True or false?
  Host A is sending Host B a large file over a TCP connection. Assume Host B has no data to send Host A. Host B will not send acknowledgments to Host A because Host B cannot piggyback the acknowledgments on data. ()
  The size of the TCP rwnd never changes throughout the duration of the connection. ()
  Suppose Host A is sending Host B a large file over a TCP connection. The number of unacknowledged bytes that A sends cannot exceed the size of the receive buffer. ()

## Slide 10
  Suppose Host A is sending a large file to Host B over a TCP connection. If the sequence number for a segment of this connection is m, then the sequence number for the subsequent segment will necessarily be m+1. ()
  The TCP segment has a field in its header for rwnd. ()
  Suppose that the last SampleRTT in a TCP connection is equal to 1 sec. The current value of TimeoutInterval for the connection will necessarily be ≥ 1 sec. ()
  Suppose Host A sends one segment with sequence number 38 and 4 bytes of data over a TCP connection to Host B. In this same segment the acknowledgment number is necessarily 42. ()